## Slide 1: CUDA Computer Division Bhabha Atomic Research Centre
Notes: 1

## Slide 2: CUDA
Compute Unified Device Architecture
NVIDIA GPU
Allows developers to use GPUs for general-purpose computing
  Write code that can be executed in parallel across multiple GPU cores
  Speeds up compute-intensive applications for parallelizable parts of a computation
High level Language
  Extended C
Notes: 2

## Slide 3: GPU as Co–processor
GPU as Compute device
  Own Memory
  Run multiple threads in parallel
Application runs on host
The compute intensive, data-parallel part is sent to GPU
  Written as C functions – Kernel
  Kernel is executed on device simultaneously by multiple threads
Notes: 3

## Slide 4: GPU Execution
Main Memory
GPU Memory
Copy Input Data
from Host to
GPU Memory
Load/Initialize
Input Data
Process Input
Data and
Write to
output
Copy Output
from GPU to
Host Memory
Host application
GPU kernel

## Slide 5: Heterogeneous Programming
Serial Code
  Executed on CPU
  Host Code
Parallel Code
  Executed on GPU
  Device Code
  CUDA Kernel
CPU = Host
GPU = Co-processor
Notes: 5

## Slide 6: Thread Hierarchy
Threads
Thread Block
Grid of Thread Blocks

## Slide 7: CUDA Kernel
C function
Executed N times in parallel by N CUDA threads
Execution configuration syntax
kernel_name<<< grid_size, block_size >>>(….)
  "grid_size": Represents the total number of thread blocks that will be launched on the GPU.
  "block_size": Indicates the number of threads within each individual thread block.
Notes: 7

## Slide 8: CUDA Example
C
void vecAdd(float A[],
float B[],
float C[])
{
for(int i = 0; i < n; i++)
{
C[i] = A[i] + B[i];
}
}
int main()
{
// Declare A,B,C
// Assign values to A and B
vecAdd(A, B, C);
}
CUDA
// Kernel definition
__global__ void vecAdd(float* A, float* B, float* C)
{
int i = threadIdx.x;
C[i] = A[i] + B[i];
}
int main()
{
// Kernel invocation
vecAdd<<<1, n>>>(A, B, C);
}
Kernel invocation from host
Number of CUDA threads specified using <<<…>>>

## Slide 9: CUDA Kernel
Unique Thread ID
Accessible within the kernel through the built-in threadIdx variable
Function Qualifier
“__global__” qualifier declares a function as a Kernel
Each thread has a unique thread ID
__global__ void vecAdd(float* A, float* B, float* C)
{
int i = threadIdx.x;
C[i] = A[i] + B[i];
}
Notes: Code in a Kernel function is executed by all the threads invoked in a GPU.

## Slide 10: Thread Hierarchy
Block
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Thread block – Organized threads
Block – 1D, 2D or 3D array of threads
Specified during kernel invocation
threadIdx
  3 component vector
  Specify ids in 3D
Invoke kernels on 2D & 3D matrices

## Slide 11: dim3 Type
CUDA defined structure of unsigned integers
struct dim3 {x; y; z};
Specify dimensions of
  Thread blocks
  Grid of thread blocks
Unspecified component – Initialized to 1
  dim3(100) – dim3(100, 1, 1)
Used both in Host side code & Kernel side code

## Slide 12: Thread Block
Threads within a block can share data among themselves through shared memory.
All threads within a block are expected to run on single Stream Multiprocessor (SM).
Number of threads per block is restricted by memory resource of single SM.
Limit of 1024 threads in a block on current GPUs
How to run more than 1024 threads?
  Grid of Thread Blocks
Notes: 12

## Slide 13: Grid of Thread Blocks
Thread blocks are equally shaped.
Multiple thread blocks execute kernel in parallel.
Thread blocks are arranged in grid
Grid can be 1D, 2D or 3D.
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Block
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)

## Slide 14: Grid of Thread Blocks
blockIdx
  Identify block within grid
  1D, 2D or 3D index
Thread block dimensions – blockDim
Grid of Thread Blocks dimension – gridDim

## Slide 15: 1D Thread Block Example
int i = blockIdx.x * blockDim.x + threadIdx.x;
Assuming blockDim.x = 64
a[0]
a[63]
a[64]
a[127]
a[128]
a[191]
blockIdx.x =0
blockIdx.x =1
blockIdx.x =2
threadIdx.x 0
threadIdx.x 63
threadIdx.x 0
threadIdx.x 63
threadIdx.x 0
threadIdx.x 63
i = 0
i = 63
i = 64
i = 127
i = 128
i = 191
….
….
….

## Slide 16: 1D Thread Block Example
__global__ void addition (float *A, float * B, float *C, int iSize)
{
// Calculate vector index.
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < iSize) // index within vector size
C[i] = A[i] + B[i];
}

## Slide 17: 2D Thread Block Example
2D array
  Rows
  Columns
1D array
  Index
2D array – 1D array
  Row No* Total Columns + Column No
R-1 and C-2
  1*3 + 2 = 5
R-2 and C-1
  2*3 + 1 = 7
 | C-0 | C-1 | C-2 | Column
R-0 | 1 | 2 | 3 | 
R-1 | 4 | 5 | 6 | 
R-2 | 7 | 8 | 9 | 
Row |  |  |  | 
1D Index |  |  |  |  |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9

## Slide 18: 2D Thread Block Example
Example of 2D block
// Add two matrices A and B of
//dimension NxN and store the
// result into matrix C
__global__ void matAdd(int N, float* A, float* B, float* C)
{
int i = threadIdx.x;
int j = threadIdx.y;
C[j * N + i] = A[j * N + i] + B[j * N + i];
// C[i][j] = A[i][j] + B[i][j];
}
// host code
int main()
{
// Declare, allocate and initialize
// device memory A, B & C
// Kernel invocation
dim3 Block(N, N);
matAdd<<<1, Block>>>(N, A, B, C);
}

## Slide 19: Execution Configuration Syntax
// Define a logical thread block.
dim3 Block(…);
eg dim3 Block(N, N, N);
// Define a logical grid.
dim3 Grid(…);
eg dim3 Grid(N, N, N);
// Launch CUDA kernel.
kernel<<<Grid, Block>>>(…);
eg matadd<<< Grid, Block>>>(N,A,B,C);

## Slide 20: Managing Device Memory
cudaMallocManaged
cudaDeviceSynchronize
cudaFree

## Slide 21: Device Memory Allocation
cudaMallocManaged()
  Allocates object in device’s Global Memory and host Memory
  Pool of managed memory is created
    It is shared between CPU and GPU
  Accessible to both CPU and GPU using single pointer
  Two parameters
    Address of a pointer to allocated object
    Size of allocated object

## Slide 22: Free Device Memory
cudaFree()
  Free object from device’s and host’s Memory
  Parameter – Pointer to object to be freed

## Slide 23: Device Memory Allocation
Example code:-
  Allocate and free an array of 256 floating point elements in device memory as well as on the host
float* Ptr;
cudaMallocManaged((void**)&Ptr, 256 * sizeof (float));
// free this memory
cudaFree(Ptr);
We cast it into double pointer because it's a pointer to the pointer. It has to point to a pointer in GPU memory.
Notes: What cudaMalloc() does is that it allocates a memory pointer on GPU, which is then pointed by the first argument we give.

## Slide 24: Synchronize Device Memory
cudaDeviceSynchronize()
  Forces the GPU to complete all pending operations, including kernel launches and memory transfers, before the host program proceeds.
  Ensures host program does not attempt to access data on the GPU until all previous operations have been completed, preventing potential data corruption or inconsistencies.

## Slide 25: CUDA Matrix Addition Example
// Add two matrices A and B
// Dimension NxN
// Store the result into C
__global__ void matAdd(int N, float* A, float* B,
float* C)
{
int i = threadIdx.x;
int j = threadIdx.y;
C[j * N + i] = A[j * N + i] + B[j * N + i];
// C[i][j] = A[i][j] + B[i][j];
}

## Slide 26: CUDA Matrix Addition Example
// host code
int main()
{
// Declare, allocate and
// initialize host data pointer.
float *A, *B, *C;

## Slide 27: CUDA Matrix Addition Example
// Allocate unified memory
cudaMallocManaged((void**)&A, N * N * sizeof (float));
cudaMallocManaged((void**)&B, N * N * sizeof (float));
cudaMallocManaged((void**)&C, N * N * sizeof (float));

## Slide 28: CUDA Matrix Addition Example
// Assign values to matrices A and B
// Kernel invocation
dim3 dimBlock(N, N);
matAdd<<<1, dimBlock>>>(N, A, B, C);
cudaDeviceSynchronize();
// Print out the results here

## Slide 29: CUDA Matrix Addition Example
cudaFree(A);
cudaFree(B);
cudaFree(C);
}

## Slide 30: Memory Hierarchy
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Registers
Local memory
Shared memory
Global memory
Read only constant memory
Read only texture memory

## Slide 31: Host Accessible Memory
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Global memory
Constant memory
Texture memory
Notes: Texture caches are designed for graphics applications where memory access patterns exhibit a great deal of spatial locality. In a computing application, this roughly implies that a thread is likely to read from an address “near” the address that nearby threads read

## Slide 32: Parallel Computing using CUDA
Allocate device memory for input data
Copy input data from host memory to device memory
Allocate device memory for output data
for each logical block within data do
for each thread within logical block do
calculate output value in device memory
Synchronize threads
Copy results from device memory to host memory
Free device memory allocated for input & output data
Notes: 32

## Slide 33: CUDA Installation
CUDA Toolkit
  Develop CUDA application
  Super user
CUDA SDK
  Sample projects
  Regular user
Notes: 33

## Slide 34: CUDA Code Compilation
Host code
  C, C++ code – .c, .cxx, or .cpp extension
  Native compiler – gcc, nmake
Device code
  Extended C – .cu extension
  nvcc compiler
Example
  nvcc -o matrixAddition matrixAddition.cu
Notes: 34

## Slide 35: CUDA Matrix Multiplication Example
//Header Files
#include <stdio.h>
#include <math.h> // math functions
#include <cuda_runtime_api.h> // CUDA runtime API
// define logical thread block size
#define N 40
#define BLOCK_SIZE 10
Notes: 35

## Slide 36: CUDA Matrix Multiplication Example
//CUDA KERNEL
__global__ void mul (float *A, float * B, float *C, int size)
{
int ROW = blockIdx.y*blockDim.y+threadIdx.y;
int COL = blockIdx.x*blockDim.x+threadIdx.x;
// Calculate matrix multiplication of 1 row
if (ROW < size && COL < size) {
float sum=0.0;
for (int i = 0; i < size; i++) {
sum += A[ROW * size + i] * B[i * size + COL];
}
C[ROW * size + COL]=sum;
}
}
Notes: 36

## Slide 37
// Vectors Using Unified Memory
// Create float pointers.
float *A, *B, *C;
// Calculate data size in no of bytes.
int iByteSize= N * N *sizeof(float);
// Allocate Unified Memory
// Accessible from CPU or GPU.
cudaMallocManaged(&A, iByteSize);
cudaMallocManaged(&B, iByteSize);
cudaMallocManaged(&C, iByteSize);
CUDA Matrix Multiplication Example
Notes: 37

## Slide 38: CUDA Matrix Multiplication Example
// Initialize Vectors
for(int i=0; i < N * N; i++)
{
// Initialize vectors.
A[i] = (float) rand() / (float) rand();
B[i] = (float) rand() / (float) rand();
C[i]=0.0;
}
Notes: 38

## Slide 39
// Execution Configuration Syntax
//N=40, BLOCK_SIZE=10
// Define a logical block size.
dim3 Block(BLOCK_SIZE, BLOCK_SIZE);
// Define a logical grid size.
dim3 Grid(ceil(N/BLOCK_SIZE), ceil(N/BLOCK_SIZE));
// Launch CUDA kernel.
mul<<<Grid,Block>>>(A, B, C, N);
CUDA Matrix Multiplication Example
Notes: 39

## Slide 40: CUDA Matrix Multiplication Example
// Wait for GPU to finish before accessing on host.
cudaDeviceSynchronize();
//Print Results
for (long i = 0; i < N; i++) {
for (long j = 0; j < N; j++) {
printf("%f ", C[i * N + j]);
}
printf("\n");
}
// Free memory.
cudaFree(A);
cudaFree(B);
cudaFree(C);
Notes: 40

## Slide 41: Questions?
Thank you