## Slide 1: Graphics Processing Unit
Computer Division
Bhabha Atomic Research Centre

## Slide 2: Topics
Evolution of Performance
Applications of GPU
CPU v/s GPU
GPU as a Co-processor
Heterogeneous Computing
GPU Architecture
Streaming Multiprocessor
Memory Hierarchy
Thread Hierarchy

## Slide 3: Evolution of Performance (1)
Early Processors:
  Single core
  Increase clock speed
    Number of cycles per second
    Number of instructions per second
  Faster execution of individual instructions
  Limitations of Clock Speed
    Physical limits on clock speeds
    Power or heat dissipation

## Slide 4: Evolution of Performance (2)
Multi Core Architecture:
  Multiple cores on Single chip
  Parallel execution of tasks
  Significant overall performance improvement
  Multiple cores – Different threads – Simultaneous execution
  Multi threaded tasks – Performance improvement
  Power Efficiency:
    Individual cores
    Lower clock speed
    Better power efficiency

## Slide 5: Evolution of Performance (3)
Heterogeneous Computing
  GPU – Graphics Processing Unit
  Specialized processor
    Process large amounts of data
    High performance
    Many core processors
    Very high memory bandwidth
    TeraFLOPs peak performance
  Single Instruction Multiple Data (SIMD)
  Offload computationally intensive tasks to GPU

## Slide 6: Evolution of Performance (4)

## Slide 7: Applications of GPU
Computer Graphics – Image Synthesis
    Generates images – Video games, Animated movies
    X-ray computed tomography
Image Processing
    Image analysis – Template matching, SURF features
High Performance Computing
    Computational Fluid Dynamics (CFD), Molecular Dynamics
AI/ML
    Deep Learning – Object detection, object recognition, image segmentation
    Large Language Models (LLM) – ChatGPT, Llama

## Slide 8: CPU v/s GPU

## Slide 9: CPU v/s GPU
Central Processing Unit – CPU
Less number of cores (~100)
Low compute density
Low latency
Higher clock speed
Powerful cores
Serial instruction processing
Handful of operations at once
Suitable for serial instruction processing
Versatility - Can be used for tasks such as OS or I/O etc
Graphics Processing Unit – GPU
Large number of cores (~5000)
High compute density
High throughput
Lower clock speed
Weak cores
Parallel instruction processing
Thousands of operations at once
Not suitable for serial instruction processing
Not Versatile – Cannot be used for tasks such as OS or I/O etc

## Slide 10
GPU as Co-processor
GPU as Compute device
  Has its own DRAM
  Can run multiple threads in parallel
Application runs on host
The compute intensive, data-parallel part is sent to GPU
  Written as C functions called kernel
  The kernel is executed on device simultaneously by multiple threads

## Slide 11: Heterogeneous Computing
Serial Code
    Executed on CPU
    Host Code
Parallel Code
    Executed on GPU
    Device Code
    Kernel
CPU – Host
GPU – Co–processor

## Slide 12: Heterogeneous Computing
Step 1: Initialize the memories on both CPU and GPU.
Step 2: Transfer the data to a GPU.
Step 3: Do the computation on a GPU.
Step 4: Transfer the data back to a CPU.
Step 5: Delete the memories on both CPU and GPU.

## Slide 13: Typical Execution
Host Memory
Device Memory
Host (CPU)
Device (GPU)
Data is copied from the host memory to the device memory via PCIe Bus
1
Host launches kernel on the device
2
The kernel is executed by multiple threads concurrently
3
The data within the device is accessed by threads through memory hierarchy
4
The results are moved back to the device memory and are transferred back to the host via PCIe bus
5
PCIe

## Slide 14: GPU Architecture
L2
L1
Shared Memory
SM
NVIDIA FERMI
Load/Store address width 64 bits. Can calculate addresses of 16 threads per clock.
16 Stream Multiprocessors (SM) 512 CUDA cores (32/SM)
IEEE 754-­‐2008 floating point (DP and SP)
6 GB GDDR5 DRAM (Global Memory)
ECC Memory support
Two DMA interface
Reconfigurable L1 Cache and Shared Memory
48 KB / 16 KB
L2 Cache 768 KB

## Slide 15: Streaming Multiprocessor
Streaming or Thread Processor
8 or 32 cores per SM
Double Precision Unit
Special Function Unit
Shared Memory
Cache memory – L1 and L2 cache

## Slide 16: Memory Hierarchy
Shared Memory per Block
Global Memory
Local Memory per Thread
Thread
Block
Grid 0
Grid 1
Shared memory
Visible to all the threads in a block
Global memory
Visible to all the threads Visible to host
Accessible to multiple kernels
Data is stored in row major order
Constant memory (Read Only)
Visible to all the threads in a block
Registers
Constant Memory
Private memory
Visible only to the thread

## Slide 17: Host Accessible Memory
Host have access to
  Global memory
  Constant memory
  Texture memory
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
Notes: Texture caches are designed for graphics applications where memory access patterns exhibit a great deal of spatial locality. In a computing application, this roughly implies that a thread is likely to read from an address “near” the address that nearby threads read

## Slide 18: Thread Hierarchy

## Slide 19: Thread Hierarchy
Threads
Thread Block
Grid of Thread Blocks

## Slide 20: Questions?
Thank you