## Slide 1: Graphics Processing Unit
Pritam Prakash Shete
Computer Division
Bhabha Atomic Research Centre

## Slide 2: Topics
Introduction
CPU v/s GPU
Heterogeneous Computing
GPU Architecture
Streaming Multiprocessor
Memory Hierarchy
Thread Hierarchy

## Slide 3: Introduction
Computer graphics – Image synthesis
Image processing – Image analysis
GP-GPU – General Purpose computation on GPU
Graphics Processing Unit – GPU
  High performance
  Many core processors
  Very high memory bandwidth
  TeraFLOPs peak performance
Single Instruction Multiple Data parallelism
Offload computationally intensive tasks to GPU

## Slide 4: CPU v/s GPU
Image ack – Google

## Slide 5: CPU v/s GPU
Central Processing Unit – CPU
Less number of cores (~100)
Low compute density
Low latency
Higher clock speed
Powerful cores
Serial instruction processing
Handful of operations at once
Graphics Processing Unit – GPU
Large number of cores (~1000)
High compute density
High throughput
Lower clock speed
Weak cores
Parallel instruction processing
Thousands of operations at once

## Slide 6: Heterogeneous Computing
Image ack – Google
Serial Code
  Executed on CPU
  Host Code
Parallel Code
  Executed on GPU
  Device Code
  Kernel
CPU – Host
GPU – Co–processor

## Slide 7: Heterogeneous Computing
Step 1: Initialize the memories on both CPU and GPU.
Step 2: Transfer the data to a GPU.
Step 3: Do the computation on a GPU.
Step 4: Transfer the data back to a CPU.
Step 5: Delete the memories on both CPU and GPU.

## Slide 8: GPU Architecture
Image ack – Google
Streaming Multiprocessor – SM
Number of SMs
Shared memory
Cache memory – L1 and L2 cache
Device memory

## Slide 9: Streaming Multiprocessor
Image ack – Google
Streaming or Thread Processor
8 or 32 cores per SM
Double Precision Unit
Special Function Unit
Shared Memory

## Slide 10: Memory Hierarchy
Image ack – Google
Local memory
Register memory
Shared memory
Global memory
Constant memory
Texture memory

## Slide 11: Thread Hierarchy
Image ack – Google

## Slide 12: Thread Hierarchy
Image ack – Google
Grid of Thread Blocks
Logical Grid
Logical Thread Block
Threads

## Slide 13: Questions?
Thank you